Push button
- Power Rating MAX: 50mA 24VDC
- Contact Resistance: MAX 100 mΩ
- Insulation Resistance: 100MΩ Min. at 100VDC
- Operating Temperature Range: -20～+70 ℃
- Storage Temperature Range: -40～+85 ℃
- Type of Operation: Tactile Feedback
- Circuit Configuration: Push-On Momentary, 1 pole-1 throw
- Dielectric Withstanding Voltage: 250VAC for 1 minute
- Operating Force: 0.95 N
- Throw Configuration: SPST
- Actuator Type: Standard
- Mounting Type: Through Hole
- Termination Style: Solder Pin
- Color: Black
- Dimensions:
- Length 6 mm
- Width 6 mm
- Height 5 mm